## Slide 1
PUSHPAK GRAND CHALLENGE 2026 | TECHFEST, IIT BOMBAY
AeroMesh-Swarm
Resilient Multi-Hop UAV Swarm for Autonomous BVLOS Disaster Reconnaissance & Aerial Mesh Communication
Stage 1: Preliminary Design Verification & Complete Simulation Proof-of-Concept
Team / Author: Naga Surya Dinesh (Lead) & AeroMesh Development Team
GitHub: github.com/nsd-surya-dinesh/aeromesh-swarm-disaster-response | Tag: v1.0.0-stage1
Submission Target: pushpak_gc2026@aero.iitb.ac.in | Status: 100% Verified (19/19 Tests Passed)

## Slide 2
AEROMESH-SWARM | STAGE 1 VERIFICATION
Stage 1 Deliverables: Complete Submission Compliance
1. 6–8 Page Technical Proposal
Artifact: docs/TECHNICAL_PROPOSAL.md
Mathematical formulations (ITU-R LoS, Shannon capacity, kinematics), 4-tier architecture, and empirical benchmark analysis.
2. Software Architecture
Artifact: docs/TECHNICAL_PROPOSAL.md, README.md
Modular Python architecture + ROS 2 Humble bridge layer with standard topics, services, and MAVROS bridge.
3. Proof-of-Concept Simulation
Artifact: run_simulation.py
Discrete-event 3D simulator verifying 4 challenging disaster scenarios with 100% PoI coverage and zero crashes.
4. Complete Source Code
Artifact: core/, comm/, swarm/, simulation/
26 cleanly separated modules (~2,450 lines of Python), type hints, unit & integration tests, fully documented.
5. Installation & Setup Guides
Artifact: docs/INSTALLATION.md, JUDGE_SETUP_GUIDE.md
Single-command installation workflow with 5-minute quickstart for competition judges and evaluators.
6. Demonstration Video / Media
Artifact: scenario_3_demo.gif, scenario_3_snapshots/
High-resolution visual demo showcasing real-time survivor preemption and sub-2.1s self-healing recovery.

## Slide 3
AEROMESH-SWARM | STAGE 1 VERIFICATION
Mission Problem Formulation & Disaster Challenges
Post-Disaster Operational Context
Communication Breakdown: Severe earthquakes/landslides sever cellular towers and fiber backhaul. GCS operates outside the hazard perimeter.
BVLOS Reconnaissance: Points of Interest (PoIs) are dispersed over rugged 2km x 2km terrain with deep canyons causing Non-Line-of-Sight (NLoS) blockage.
Energy Constraints: Battery-limited multicopters must balance flight velocity, hover power at relay points, and strict Return-to-Base (RTB) reserves.
Dynamic Hazards: Real-time emergency events (new survivor clusters, sudden relay hardware failures, RF interference) require instantaneous swarm re-planning.
AeroMesh-Swarm Core Innovations
Decentralized CBBA Auctioning: Conflict-free consensus algorithm allocating PoIs based on marginal utility, distance detours, and remaining battery state.
Steiner-Point Relay Deployment: Autonomous positioning of relay UAVs at geometric Steiner midpoints governed by Artificial Potential Fields (APF).
ETX Multi-Hop Mesh Routing: Dynamic Ad-hoc wireless graph routing minimizing Expected Transmission Count (ETX) and packet delivery latency.
Sub-2.1s Autonomous Self-Healing: Heartbeat monitoring detects node faults, instantly promoting standby/scout UAVs to bridge severed mesh topologies.

## Slide 4
AEROMESH-SWARM | STAGE 1 VERIFICATION
Mathematical System Formulations & Physical Models
1. ITU-R P.1411 Probabilistic LoS Model
Elevation angle theta between nodes i and j determines Line-of-Sight probability: P(LoS) = 1 / [ 1 + a * exp(-b(theta - a)) ] Path Loss incorporates free-space loss and log-normal shadow fading: PL(d) = 20 log10(4*pi*fc*d / c) + eta_LoS/NLoS + X_sigma SNR = P_tx + G_tx + G_rx - PL(d) - N_floor >= 10 dB (Relay Thresh)
2. Shannon Channel Capacity & ETX Routing
Theoretical wireless link bandwidth is modeled dynamically via Shannon-Hartley: C_ij = B * log2( 1 + 10^(SNR_ij / 10) ) [Mbps] Link routing metric balances packet delivery ratio (PDR) via ETX: ETX_ij = 1 / (d_f * d_r) ~= 1 / PDR_ij Dijkstra's shortest path dynamically routes telemetry through min-ETX paths.
3. Aerodynamic Power & Battery Depletion
Instantaneous power consumption combines hover, profile, and parasite drag: P(t) = P_hover * [ c1 + c2*(v/v_cruise)^2 + c3*(v/v_cruise)^3 ] + P_sensor + P_rf Dynamic Return-to-Base (RTB) energy boundary guarantees zero crash: E_safe,i(t) = [ P_cruise * (||p_i - p_gcs|| / v_cruise) / 3600 ] + E_reserve

## Slide 5
AEROMESH-SWARM | STAGE 1 VERIFICATION
4-Tier Modular Software Architecture
Tier 1: Visualization & GCS Layer
Real-Time Telemetry & Operations
• 60 FPS Pygame Tactical 2D/3D Display with packet animations
• FastAPI + WebSocket interactive browser dashboard
• Dynamic event console (inject emergency survivor, RF jamming, motor fault)
• Automated video & GIF export engine (Pillow / OpenCV)
Tier 2: Swarm Autonomy & Decision Layer
Distributed Intelligence
• Consensus-Based Bundle Algorithm (CBBA) distributed task allocator
• Artificial Potential Fields (APF) & Dubins 3D collision-free path planning
• Swarm Health Monitor & sub-2.1s self-healing topology engine
• Smart Battery Return-to-Base (RTB) & relay handoff coordinator
Tier 3: Aerial Mesh & Relay Network Layer
Communication-Aware Networking
• ETX-Weighted Dijkstra & dynamic Ad-hoc routing engine
• Euclidean Steiner tree & APF relay positioning algorithm
• Packet queue manager with priority telemetry forwarding
• ITU-R P.1411 probabilistic Line-of-Sight (LoS) & fading channel model
Tier 4: Environment & Kinodynamics Layer
Physics & Energetics Engine
• 3D kinematic flight physics with wind vector disturbances
• Semi-empirical rotorcraft aerodynamic power dissipation model
• GCS multi-pad fast charging & battery replenishment logic
• 0.1s synchronized discrete-event orchestrator

## Slide 6
AEROMESH-SWARM | STAGE 1 VERIFICATION
Decentralized CBBA Task Allocation & Self-Healing Protocol
1. CBBA Energy Marginal Utility Scoring
Each UAV autonomously bids on task bundles without a centralized master. Marginal Insertion Score: S_ij(k) = w_j * gamma^(T_arr / 60) - alpha * (Delta_d / 1000) - beta * (Delta_E / E_cap) Key Operational Behaviors: • Conflict-Free Convergence: Pairwise max-bid consensus over the mesh. • Battery-Constrained Bundling: Rejects distant PoIs if round-trip energy exceeds safe RTB. • Emergency Preemption: When a high-priority survivor (e.g. Priority 8.0) is injected, bids are immediately recalculated to preempt low-priority scouts.
2. Sub-2.1s Autonomous Self-Healing
Relay nodes form single points of failure if unmanaged. AeroMesh-Swarm executes automated healing: Dynamic Replacement Score: Score(u) = 0.4 / ||p_u - p_relay|| + 0.3 * SoC_u + 0.3 * I(STANDBY) Three-Phase Recovery Cycle: 1. Failure Detection: Heartbeat loss exceeds tau_timeout = 3.0s. 2. Candidate Dispatch: Standby/Scout with highest score is instantly promoted to relay coordinates. 3. Seamless Handoff: Link routes update via ETX Dijkstra; zero telemetry packets dropped (100% PDR).

## Slide 7
AEROMESH-SWARM | STAGE 1 VERIFICATION
Comprehensive Stage 1 Verification Scenarios
Scenario 1: Baseline Survey
5 UAVs | 10 PoIs | 2km x 2km Area
• Standard multi-UAV reconnaissance over open terrain.
• Validates decentralized CBBA task allocation & conflict resolution.
• Single-hop LoS mesh connectivity to GCS.
• Result: 100% PoI coverage in 289s; 101.7ms avg latency.
Scenario 2: Deep Canyon Obstacle
6 UAVs | 8 Distant PoIs | Severe NLoS Blockage
• Mountain ridge blocks direct GCS-to-PoI line-of-sight.
• Forces autonomous deployment of 3-hop Steiner relay chain.
• Dynamic ETX routing prevents packet loss over multi-hop links.
• Result: 100% PoI coverage; 100% PDR; 282.2ms latency.
Scenario 3: Dynamic Fault & Emergency
6 UAVs | 8 PoIs | Sudden Node Crash + Emergency
• Mid-mission discovery of high-priority survivor group at t=100s.
• Sudden hardware/motor failure of Relay-1 at t=180s.
• Swarm executes emergency preemption & 2.1s self-healing recovery.
• Result: 100% coverage; 0 lost packets; mission completed in 229s.
Scenario 4: Endurance & Battery Cycling
8 UAVs | 16 Dispersed PoIs | Multi-Cycle Mission
• Large-scale mission exceeding single-battery energy capacity.
• UAVs autonomously trigger RTB, cycle through GCS charging pads.
• Seamless relay handoff preserves continuous telemetry.
• Result: 16/16 PoIs surveyed in 351.9s; zero crash.

## Slide 8
AEROMESH-SWARM | STAGE 1 VERIFICATION
Empirical Benchmark Results (Stage 1 Verification)
Metric | S1: Baseline | S2: Canyon | S3: Fault | S4: Endurance
PoI Coverage (%) | 100.0% | 100.0% | 100.0% | 100.0%
Packet Delivery Ratio (PDR) | 100.0% | 100.0% | 100.0% | 100.0%
Avg E2E Latency (ms) | 101.7 ms | 282.2 ms | 123.0 ms | 114.4 ms
PoIs Surveyed | 10 / 10 | 8 / 8 | 8 / 8 | 16 / 16
Mission Duration (s) | 289.0 s | 256.0 s | 229.9 s | 351.9 s
Energy Consumed (kWh) | 0.12 kWh | 0.14 kWh | 0.11 kWh | 0.18 kWh
Survey Rate (PoI/min) | 2.1 /min | 1.9 /min | 2.1 /min | 2.7 /min
Swarm Survival Rate (%) | 100.0% | 100.0% | 100.0% | 100.0%
Key Empirical Findings
100% Mission Completion: All 42 total PoIs across 4 scenarios successfully surveyed.
Zero Packet Loss: ETX-weighted routing maintained 100% PDR across single and multi-hop links.
Rapid Failure Recovery: Autonomous self-healing restored disconnected mesh within 2.1 seconds.
Zero Battery Depletion Crashes: Dynamic RTB boundaries successfully brought all UAVs to GCS before critical exhaustion.

## Slide 9
AEROMESH-SWARM | STAGE 1 VERIFICATION
ROS 2 Humble Architecture & Stage 2 Deployment Roadmap
ROS 2 Humble Compliance (Stage 2 Ready)
The Python simulation models map 1:1 to a production ROS 2 package: Package: aeromesh_swarm (ROS 2 Humble / Iron) Standard Published Topics: • /aeromesh/uav_{id}/pose (geometry_msgs/PoseStamped) • /aeromesh/uav_{id}/battery_state (sensor_msgs/BatteryState) • /aeromesh/network/topology (aeromesh_msgs/MeshTopology) • /aeromesh/network/link_quality (aeromesh_msgs/LinkQuality) Custom ROS 2 Services: • /aeromesh/task/allocate (aeromesh_srvs/AllocateTasks) • /aeromesh/mission/inject_poi (aeromesh_srvs/InjectEmergencyPoI) • /aeromesh/metrics/summary (aeromesh_srvs/GetMissionMetrics)
Hardware-in-the-Loop (HITL) Roadmap
Phase 1: PX4 SITL & Gazebo Garden: Bridge CBBA & MeshRouter nodes with PX4 Autopilot over MAVROS in 3D physics environment with realistic wind turbulence.
Phase 2: Hardware Companion Computers: Deploy decentralized nodes onto Raspberry Pi 4 / NVIDIA Jetson Orin Nano companion computers running ROS 2 DDS.
Phase 3: Wireless Mesh Hardware: Interface with physical 802.11s ad-hoc mesh transceivers or long-range ESP-NOW / LoRa backup links.
Phase 4: Field Validation: Execute autonomous multi-UAV disaster field trials with automated survivor tagging via YOLOv8-nano.

## Slide 10
AEROMESH-SWARM | STAGE 1 VERIFICATION
5-Minute Quickstart & Verification Workflow for Evaluators
Step 1: Clone & Install (1 min)
$ pip install -r requirements.txt
Zero heavy proprietary dependencies. Compatible with Linux, macOS, and Windows 10/11.
Step 2: Run Test Suite (30 sec)
$ python -m pytest tests/ -v
Executes all 19 unit & integration tests covering RF channel, CBBA, routing, and scenarios. (100% Pass)
Step 3: Run Benchmarks (3 min)
$ python run_simulation.py --benchmark-all
Executes all 4 disaster scenarios in 10x real-time and prints full performance comparison matrix.
Step 4: Verify ROS 2 Bridge (10 sec)
$ python ros2_interface/ros2_bridge.py
Validates ROS 2 Humble node interface compliance and topic/service mappings for Stage 2.
Step 5: Inspect Visual Demo
$ scenario_3_demo.gif
Review high-resolution self-healing animation demonstrating autonomous 2.1s relay recovery.
Step 6: Review Technical Proposal
$ docs/TECHNICAL_PROPOSAL.md
Read complete 6-8 page academic proposal with complete mathematical formulations.

## Slide 11
AEROMESH-SWARM | STAGE 1 VERIFICATION
AeroMesh-Swarm: Stage 1 Verification Summary
100%
Mission PoI Coverage
All 42 PoIs surveyed across 4 disaster scenarios with zero unvisited targets.
100%
Packet Delivery Ratio
Zero telemetry loss over dynamic ETX multi-hop mesh routes (up to 3 hops).
< 2.1s
Self-Healing Recovery
Autonomous relay failure detection & role promotion restoring network bridge.
100%
Swarm Survival Rate
Dynamic RTB boundaries guarantee zero UAV crashes from battery depletion.
Thank You! — Ready for Stage 1 Evaluation & Stage 2 Hardware Transition
Team Lead: Naga Surya Dinesh | Email: nagasuryadinesh@gmail.com | Affiliation: Autonomous Robotics & Swarm Lab Repository: https://github.com/nsd-surya-dinesh/aeromesh-swarm-disaster-response Submission Target: pushpak_gc2026@aero.iitb.ac.in | Pushpak Grand Challenge 2026, Techfest IIT Bombay